## Slide 1: Project for Wireless Mesh network channel assignment
CSE 812
Xiaoyan Li, Zhongzheng Chen, Chang Liu

## Slide 2: Wireless Mesh network-multi-channel-unicast

## Slide 3: Mesh network problems
Mesh network optimization
Network performance metric
Interference problem
Routing approaches
Static or dynamic
Load topology
Link optimization

## Slide 4: Mesh Network optimization
Internet

## Slide 5: Is minimizing inference the same as maximizing traffic?
Internet
Channel A
Channel B
Channel C
Channel A
Channel C
Link removal also results in graph partition, channel assignment and routing approach problems
Hassen A, Mohamed O, Shamala S, Nor A, 2016

## Slide 6: Link optimization methods
Spanning tree link optimization
Traffic profile link optimization
Flow-based link optimization
Power control link optimization
High quality metric link optimization
Raniwala and Chiueh, 2005; Kim and Suh, 2010
Skalli et al., 2007; Subramanian et al., 2008
Chiu et al., 2009; Mogaibel et al., 2012
Chaudhry et al., 2012
Draves et al. 2004

## Slide 7: Interference
Node A
Node B
Node C
Channel 1
Channel 1
Node C
Node D
Channel 1
Node A
Node B
Channel 1
Node A
Node B
Channel 1
Node C
Channel 1
Node D
Intra-flow interference
Inter-flow inference
Rate inference
External source inference
Hidden node inference
Node C
Node D
Channel 1
Channel 1
External source
Node C
Node D
Low rate Channel 1
Node A
Node B
High rate Channel 1

## Slide 8: Load topology
Logic topology
Traffic topology
Routing strategy
Interference

## Slide 9
Internet
Internet
Logical Topology
Known traffic Topology

## Slide 10: Static or Dynamic
Load
Dynamic or static
Dynamic load
Logic graph
Logic graph dynamic
routing
Routing dynamic
Routing static
Logic graph static
routing
Routing dynamic
Routing static
Static load
Static solution

## Slide 11: Static or Dynamic
Static
Dynamic
Optimize capacity
Response time
Flexible
Flow response
Stable
No response time
Easy to implement

## Slide 12: What is the good measure?
Min interference
High flow median
High network capacity
High total flow
Node C
Node D
Channel 1
Node A
Node B
Channel 1
A
B
Internet
C
A
B
Internet
C
D
E
F
T = 5
F = 5
T = 4
F = 4
T = 3
F = 3

## Slide 13: Disagreement
Routing
Stability
Client
Fault tolerance
Connectivity
Determined by logic and load topology
Disconnect network
Load topology change
Join and switch nodes
Broken nodes

## Slide 14: Comparison of channel assignment approaches
Channel inference index
Connectivity-aware
Routing aware
Joint multicast routing

## Slide 15: Channel inference index and connectivity approach
  Minimize the total network inference which refers to the number of nodes/links sharing the same channel
Interference-aware channel assignment
  Load of each link is monitored, and the channel of congested link is updated by channel with least load
Traffic-aware channel assignment
  Sum of the end-to-end throughput of all flows used as channel assignment index. Maximize the total throughput between all pairs of nodes
Throughput-aware channel assignment
  Packet drop and blocking probability was used as metric to quantify performance of a channel. This metric is used to reduce transmission delay.
QoS-aware channel assignment
  Actual link capacity in a WMN by considering the congestions over all links was used to indicate the impact on global network performance of a single link
Capacity/data rate aware
Node connectivity in dynamic channel assignment
Node connectivity in static channel assignment

## Slide 16: Joint Routing and channel assignment approaches
  Hyacinth-based Channel Assignment
    Raniwala and Chiueh (2005)
  Load Aware Channel Assignment
    Raniwala et al. (2004)
  Maxflow-based Centralized Channel Assignment
    Skalli et al. (2007)
  Distributed Congestion-Aware Channel Assignment
    Mohsenian Rad and Wong (2009)
  Cluster-based joint Channel Assignment and Routing Protocol
    Mettali Gammar and Ghannay (2005)
  Robust Channel Assignment and Routing with Time Partitioning
    Wellons and Xue ( 2014)
  Joint Qos Routing and Channel Assignment
    Bakhshi et al. (2011)
Joint unicast and channel assignment approaches

## Slide 17: Generate Random Mesh Network Graph
Covering area: 500*500
Number of nodes: 1000
Available links: 11
Communication range: 20

## Slide 18: Generate Random Mesh Network Graph nodes locations
Wireless Mesh Network Nodes Position Matrix
Matrix dimension: 1000*3
First column is nodes id
Second column is nodes x position
Third column is nodes y position

## Slide 19: Generate Random Mesh Network Graph nodes locations
Nodes locations were generated by uniform distribution

## Slide 20: Generate Random Mesh Network Graph link matrix
Pairwise distance between all nodes were calculated based on nodes locations
  For simplicity, (1000*1000 pairs)
Nodes pairwise distance compared with communication range to determine whether it is possible to form a link or not
Link matrix dimension 1000000*5:
  The first column is link index
  The second column is first node index
  The third column is second node index
  The fourth column is pairwise distance
  The fifth column is link indicator

## Slide 21: Generate Random Mesh Network Graph link distance matrix
Distance between each pair of links were calculated
Link distance is calculated by the smallest distance
  Four pairwise distance between each pair of nodes of two links
Link distance matrix dimension #(links*links)*5
  The first column is first node id of first link
  The second column is second node id of first link
  The third column is first node id of second link
  The fourth column is second node id of second link

## Slide 22
Channel Assignment Methods

## Slide 23
Channel Assignment Strategy
Min-interference and Connectivity-Oriented Partially Overlapped Channel Assignment (MC-POCA)
Utilize partially overlapped channels instead of 3 non-overlapped channels
P. Kyasanur and N.H. Vaidya, Routing and Link-layer Protocols for Multi-Channel Multi-Interface Ad Hoc Wireless Networks, SIGMOBILE Mobile Computing and Communications Review, vol. 10, no. 1, pp.
Partially Overlapped Assignment
Start
Calculate links assignment rank
Generate decreasing links queue
End
Partially Overlapped Channel Assignment
Select channel by score function
Routing Selection

## Slide 24
Strategy Advantages
Low time complexity
Effectively utilized partially overlapped channels
Easy to assess the link interference

## Slide 25
Strategy Drawbacks
Score function 1
Count how many the link pairs which have interference for each channel
Select the best channel with the minimum interference link pairs to assign
Example of a conflict graph
Figure Scource: https://www.researchgate.net/figure/The-conflict-graph-for-the-five-node-network_fig2_51915978

## Slide 26
Strategy Drawbacks
Score function 2
Get the distance of closest nodes of 2 links
Get ir(p,l), the interference distance ratio
For any assigned links, sum interference up and then choose the best channel

## Slide 27
Strategy Drawbacks
Partially overlapped channel network may have much more interference link pairs
Node Interference range may not reasonable for calculating link interference range
Current assigned channel will interference unassigned empty links

## Slide 28
Strategy Drawbacks
Algorithm Structure
Once a link is assigned with certain channel, it’s impossible to modify or revise
The rank of links may change during the algorithm, but priority queue never update
Sequential Forward Channel Assignment
Figure Scource: https://www.cc.gatech.edu/~bboots3/CS4641-Fall2018/Lecture16/16_FeatureSelection.pdf

## Slide 29
Score Function J(w) Design
Step 1. Measure interferenced by other links
Step 2. Measure interference assigned links
Step 3. Measure interference unassigned empty links

## Slide 30
Score Function J(w) Design
Step 1. Measure interferenced by other links

## Slide 31
Score Function J(w) Design
Constraints
Define the receiver SNR as a threshold.
is predefined because wireless mesh network utilizes OQPSK or 64QAM demodulation

## Slide 32
Score Function J(w) Design
Score for Step 1
Define the function
One example of function
A(0) means all assigned links which interference range could cover link

## Slide 33
Score Function J(w) Design
Step 2. Measure interference assigned links

## Slide 34
Constraints 1
Score Function J(w) Design
For each assigned link, we can define a SNR threshold.

## Slide 35
Constraints 2
Score Function J(w) Design
Calculate total variance of assigned links

## Slide 36
Score Function J(w) Design
Score for Step 2
One example of function
B(0) means all assigned links within the interference range of link

## Slide 37
Score Function J(w) Design
Step 3. Measure interference unassigned empty links

## Slide 38
Score Function J(w) Design
Score for Step 3
is the smallest index the node appears as a receiver in the link priority queue

## Slide 39
Score Function J(w) Design
Score for Step 3
One example of function
is a discrete function which means that if assigning channel at the edge of frequency bandwidth, there will be more available partially overlapped channels for other links

## Slide 40
Score Function J(w) Design
One example of wireless mesh network

## Slide 41
Score Function J(w) Design
Wavelength Estimation
Figure Scource: https://en.wikipedia.org/wiki/List_of_WLAN_channels
Estimate as 0.12m to simplify calculation

## Slide 42
Sequential Forward Channel Assignment (SFS)
Algorithm Structure Design
Solution Space for SFS

## Slide 43
Algorithm Structure Design

## Slide 44
Drawbacks
Algorithm Structure Design
Once a link is assigned with certain channel, it’s impossible to modify or revise
The rank of links may change during the algorithm, but priority queue never update
One example of wireless mesh network

## Slide 45
Sequential Floating Forward Channel Assignment (SFFS)
Algorithm Structure Design
Solution Space for SFFS
Future work

## Slide 46: Analysis, Visualization, Evaluation
Graph based evaluation
  Random Graph
    Communication Graph
      Density Analysis
      1000 x 1000 area
      Communication range 250
    Conflict Graph
      Interference range 250

## Slide 47: Graph Analysis

## Slide 48: Fractional Network Interference
  Binary interference:
    : traffic of link
    : whether interference exist or not
  Non-binary interference:
    : interference factor between two channels

## Slide 49: Algorithm Step Visualization
Simple graph that has optimal solutions
FNI = 0.83
Rank = [100.0, 200.0, 300.0]

## Slide 50: Algorithm Step Visualization
Simple graph that has optimal solutions
FNI = 0.24
Rank = [100.0, 200.0, 300.0]

## Slide 51: Algorithm Step Visualization
Simple graph that has optimal solutions
FNI = 0.0
Rank = [100.0, 200.0, 300.0]

## Slide 52: Algorithm Step Visualization
Another graph that has can’t remove all interference
FNI = 0.91
Rank = [100.0, 166.6, 200.0, 250.0, 266.6, 600.0]

## Slide 53: Algorithm Step Visualization
Another graph that has can’t remove all interference
FNI = 0.59
Rank = [100.0, 166.6, 200.0, 250.0, 266.6, 600.0]

## Slide 54: Algorithm Step Visualization
Another graph that has can’t remove all interference
FNI = 0.36
Rank = [100.0, 166.6, 200.0, 250.0, 266.6, 600.0]

## Slide 55: Algorithm Step Visualization
Another graph that has can’t remove all interference
FNI = 0.33
Rank = [100.0, 166.6, 200.0, 250.0, 266.6, 600.0]

## Slide 56: Algorithm Step Visualization
Another graph that has can’t remove all interference
FNI = 0.21
Rank = [100.0, 166.6, 200.0, 250.0, 266.6, 600.0]

## Slide 57: Algorithm Step Visualization
Another graph that has can’t remove all interference
FNI = 0.18
Rank = [100.0, 166.6, 200.0, 250.0, 266.6, 600.0]

## Slide 58: Evaluation
Number of Nodes vs. FNI

## Slide 59: Evaluation
Number of Nodes vs. FNI

## Slide 60: Evaluation
Assigned Links vs. FNI
  100 Nodes

## Slide 61: Work Distribution
Xiaoyan Li | Chang Liu | Zhongzheng Chen
Literature review Graph generation Generate link matrix Calculate link distance based on nodes locatioss | Algorithm structure design New scoring function SFS and SFFS Algorithm implementation | Graph analysis Algorithm steps visualization Performance metric implementation

## Slide 62: Plans Next
Xiaoyan Li | Chang Liu | Zhongzheng Chen
Write abstract, introduction, related work of the report and generate graph | Write methodology, implementation details of the report | Write technical results and analysis of the report
Write future work, summary and lessons learned of the report |  | 

## Slide 63: References
Bahl, Paramvir, Ranveer Chandra, and John Dunagan. 2004. “SSCH.” Proceedings of the 10th Annual International Conference on Mobile Computing and Networking - MobiCom ’04. https://doi.org/10.1145/1023720.1023742.
Beheshtifard, Ziaeddin, and Mohammad Reza Meybodi. 2018. “An Adaptive Channel Assignment in Wireless Mesh Network: The Learning Automata Approach.” Computers & Electrical Engineering 72 (November): 79–91.
Bongsu, Raja Hasyifah Raja, Abdullah Mohammed, and Mohamad Afendee Mohamed. n.d. “Recent Trends in Channel Assignment Algorithms for Multi-Radio Multi-Channel in Wireless Mesh Network.” https://pdfs.semanticscholar.org/b6a6/810ecda50bcdbb9386d1f7f9a64006da3090.pdf.
Cheng, Hongju, Naixue Xiong, Athanasios V. Vasilakos, Laurence Tianruo Yang, Guolong Chen, and Xiaofang Zhuang. 2012. “Nodes Organization for Channel Assignment with Topology Preservation in Multi-Radio Wireless Mesh Networks.” Ad Hoc Networks. https://doi.org/10.1016/j.adhoc.2011.02.004.
Ding, Yong, Yi Huang, Guokai Zeng, and Li Xiao. 2008. “Channel Assignment with Partially Overlapping Channels in Wireless Mesh Networks.” In Proceedings of the 4th Annual International Conference on Wireless Internet, 38. ICST (Institute for Computer Sciences, Social-Informatics and Telecommunications Engineering

## Slide 64: References
Duarte, P. B. F., Z. M. Fadlullah, A. V. Vasilakos, and N. Kato. 2012. “On the Partially Overlapped Channel Assignment on Wireless Mesh Network Backbone: A Game Theoretic Approach.” IEEE Journal on Selected Areas in Communications 30 (1): 119–27.
Du, P., W. Jia, L. Huang, and W. Lu. 2007. “Centralized Scheduling and Channel Assignment in Multi-Channel Single-Transceiver WiMax Mesh Network.” In 2007 IEEE Wireless Communications and Networking Conference, 1734–39.
Ko, B., V. Misra, J. Padhye, and D. Rubenstein. 2007. “Distributed Channel Assignment in Multi-Radio 802.11 Mesh Networks.” In 2007 IEEE Wireless Communications and Networking Conference, 3978–83. Liu, Y., R. Venkatesan, and C. Li. 2009. “Channel Assignment Exploiting Partially Overlapping Channels for Wireless Mesh Networks.” In GLOBECOM 2009 - 2009 IEEE Global Telecommunications Conference, 1–5.
Meng, X., K. Tan, and Q. Zhang. 2006. “Joint Routing and Channel Assignment in Multi-Radio Wireless Mesh Networks.” In 2006 IEEE International Conference on Communications, 8:3596–3601.
Mogaibel, Hassen A., Mohamed Othman, Shamala Subramaniam, and Nor Asilah Wati Abdul Hamid. 2016. “Review of Channel Assignment Approaches in Multi-Radio Multi-Channel Wireless Mesh Network.” Journal of Network and Computer Applications 72 (September): 113–39.

## Slide 65: References
Raniwala, Ashish, Kartik Gopalan, and Tzi-Cker Chiueh. 2004. “Centralized Channel Assignment and Routing Algorithms for Multi-Channel Wireless Mesh Networks.” ACM SIGMOBILE Mobile Computing and Communications Review. https://doi.org/10.1145/997122.997130.
Raniwala, A., and Tzi-cker Chiueh. 2005. “Architecture and Algorithms for an IEEE 802.11-Based Multi-Channel Wireless Mesh Network.” In Proceedings IEEE 24th Annual Joint Conference of the IEEE Computer and Communications Societies., 3:2223–34 vol. 3.
Skalli, H., S. K. Das, L. Lenzini, and M. Conti. 2006. “Traffic and Interference Aware Channel Assignment for Multi-Radio Wireless Mesh Networks.” In Proc. of ACM Int. Conf. on Mobile Comput. and Netw (MOBICOM) Pp, 15–26.
Skalli, H., S. Ghosh, S. K. Das, L. Lenzini, and M. Conti. 2007. “Channel Assignment Strategies for Multiradio Wireless Mesh Networks: Issues and Solutions.” IEEE Communications Magazine 45 (11): 86–95.
Subramanian, A. P., H. Gupta, S. R. Das, and J. Cao. 2008. “Minimum Interference Channel Assignment in Multiradio Wireless Mesh Networks.” IEEE Transactions on Mobile Computing 7 (12): 1459–73.
Wang, J., B. Xie, K. Cai, and D. P. Agrawal. 2007. “Efficient Mesh Router Placement in Wireless Mesh Networks.” In 2007 IEEE International Conference on Mobile Adhoc and Sensor Systems, 1–9.

## Slide 66: References
Yin, Z., Z. Li, and M. Chen. 2007. “A Novel Channel Assignment Algorithm for Multicast in Multi-Radio Wireless Mesh Networks.” In 2007 12th IEEE Symposium on Computers and Communications, 283–88.
Zhao, Xiongwen, Siyuan Zhang, Liang Li, Zhaoyan Qu, Yu Zhang, Yi Ding, and Junyu Liu. 2018. “A Multi-Radio Multi-Channel Assignment Algorithm Based on Topology Control and Link Interference Weight for a Power Distribution Wireless Mesh Network.” Wireless Personal Communications 99 (1): 555–66.
Kim, S.-H., Kim, D.-W., Suh, Y.-J., 2011. A cooperative channel assignment protocol for multi-channel multi-rate wireless mesh networks. Ad Hoc Netw. 9, 893–910.
Chiu, H.S., Yeung, K., Lui, K.-S., 2009. J-car: an efficient joint channel assignment and routing protocol for IEEE 802.11-based multi-channel multi-interface mobile ad hoc networks. IEEE Trans. Wirel. Commun. 8, 1706–1715.
Mogaibel, H.A., Othman, M., Subramaniam, S., Hamid, N.A.W.A., 2012. On-demand channel reservation scheme for common traffic in wireless mesh networks. J. Netw. Comput. Appl. 35, 132–151.
Chaudhry, A., Ahmad, N., Hafez, R., 2012. Improving throughput and fairness by improved channel assignment using topology control based on power control for multi-radio multi-channel wireless mesh networks. EURASIP J. Wirel. Commun. Netw. 2012, 1–25.
Draves, R., Padhye, J., Zill, B., 2004. Routing in multi-radio, multi-hop wireless mesh networks. In: Proceedings of the 10th Annual International Conference on Mobile Computing and Networking (MobiCom 04), ACM, New York, NY, USA, pp. 114–128.